## Slide 1: Hardware and Locomotion
Adapted from
David V Lu

## Slide 2: Robot Hardware
Actuators / Motors
Sensors
Computation/Communication
Power

## Slide 3: With Great Power
Primary Hardware Concern
Trade off: Batteries vs. Cords

## Slide 4: With Great Power
Primary Hardware Concern
Trade off: Batteries vs. Cords

## Slide 5: Batteries
Heavy
Hazardous: lead/acid technology
Limited Life Span
Swapping
Batteries
Recharging

## Slide 6: Tethered Robots
Effectively unlimited power
(and communication)
Very little weight
Limits Range
Limited
Environments

## Slide 7: Boston Dynamics Cheetah

## Slide 8: Other Options
Solar
Internal Combustion

## Slide 9: More Options
Radioisotope Themoelectric Generator

## Slide 10: Locomotion
Wheels
Legs
Propellors/Wings
Thrusters/Jets

## Slide 11: Locomotion Concepts: Principles Found in Nature
R. Siegwart

## Slide 12: Locomotion Concepts
Concepts found in nature
  difficult to imitate technically
Most technical systems use wheels or caterpillars
Rolling is most efficient, but not found in nature
  Nature never invented the wheel !
However, the movement of a walking biped is close to rolling
Notes: On constate que la technologie dont nous disposons ne permet pas de reproduire des machines capables d'imiter ce que la nature à su créer. Cette dernière dispose d'outils comme la réplication cellulaire et la spécialisation qui lui permet de créer des structures complexes miniaturisées et fonctionelles. De plus le système de stockage d'énergie ainsi que les systèmes musculaires que l'on trouve dans la nature possèdent des caractéristiques de rendement qui sont nettement supérieures aux batteries et aux moteurs inventées par l'homme.
Du à ces limitations techniques, la plupart des robots mobiles crées par l'homme utilisent des roues. Il est intéressant de constater que ce mécanisme de locomotion n'était jamais apparu dans la nature avant que l'homme ne le découvre et ne le fasse évoluer. On peut tout de même constater que la marche d'un bipède peut s'apparenter à un polygone qui roule.

## Slide 13: Biped Walking
Biped walking mechanism
  not to fare from real rolling.
  rolling of a polygon with side length equal to the length of the step.
  the smaller the step gets, the more the polygon tends to a circle (wheel).
However, fully rotating joint was not developed in nature.

## Slide 14: Walking or rolling?
number of actuators
structural complexity
control expense
energy efficient
  terrain (flat ground, soft ground, climbing..)
movement of the involved masses
  walking / running includes up and down movement of COG
  some extra losses

## Slide 15: Stability
Static Stability - can balance without being active
Dynamic Stability - Needs active control to stay upright (stable when moving)

## Slide 17: Stable Configurations
Projection of the center of mass must fall within the support polygon

## Slide 18: Mobile Robots with Wheels
Wheels are the most appropriate solution for most applications
Three wheels are sufficient to guarantee stability
With more than three wheels an appropriate suspension is required
Selection of wheels depends on the application

## Slide 19: Degrees of Freedom (DOF)

## Slide 20: The Four Basic Wheels Types
a) Standard wheel: Two degrees of freedom; rotation around the (motorized) wheel axle and the contact point
b) Castor wheel: Three degrees of freedom; rotation around the wheel axle, the contact point and the castor axle
- used in office chairs

## Slide 21: The Four Basic Wheels Types
c) Swedish wheel: Three degrees of freedom; rotation around the (motorized) wheel axle, around the rollers and around the contact point
d) Ball or spherical wheel: Three degrees of freedom, around contact point in any direction
- Suspension technically not solved

## Slide 22: Ackerman Steering - Four Wheels
Two Active Fixed Wheels in Back
Two Passive Steerable Wheels in Front

## Slide 23: Bike Steering - 2 Wheels
One Active Fixed Wheel in Back
One Passive Steerable Wheel in Front

## Slide 24: Segway - 2 Wheels
Two Active Wheels
Center of Mass below Axle
Cye Personal Robot

## Slide 25: Differential Drive
Equal Wheel Velocity
Top Wheel Faster
Forward Kinematics
(more on this later)

## Slide 26: Skid Steering - Four Wheels
Four active fixed wheels

## Slide 27: Two+One - Three Wheels
Two Active Fixed Wheels in Back
Point of Contact / Castered Wheel in front

## Slide 28: Turtlebot
Two Active Wheels
One Caster Wheel
One Passive Wheel

## Slide 29: PR2 - Four Wheels
Four steerable active wheels

## Slide 30: Omniwheels
Slide Laterally With Ease

## Slide 31: Three Omniwheels

## Slide 32: Swedish / Mecanum Wheels

## Slide 33: The World is Flat!

## Slide 34: Rocker Bogie - Six Wheels

## Slide 35: Legs
Can Deal with Rough Terrain
Quality of Ground Matters Less
Can Cross Holes
Power Needs
Mechanical Complexity
More complex kinematics

## Slide 36: Mobile Robots with legs (walking machines)
The fewer legs the more complicated becomes locomotion
  Stability - at least three legs are required for static stability
During walking some legs are lifted
  thus loosing stability?
For static walking at least 6 legs are required
  babies have to learn for quite a while until they are able to stand or even walk on there two legs.

## Slide 37: Most Obvious Gaits with 4 legs
Changeover Walking Galloping
free fly

## Slide 38: Most Obvious Gait with 6 legs (static)

## Slide 39: Honda Asimo

## Slide 40: Boston Dynamics Petman

## Slide 41: 4+ Legs

## Slide 42: Spider Robot

## Slide 43: Other Robot Mobility
Sliding
Crawling
Fixed Wings
Rotary Wings